## Slide 1
Overview of the WEST ICRH Results for C5
February 2021
J.Hillairet, L.Colas and the WEST IC Team: J.M.Bernard, F.Durand, N.Faure, P.Garibaldi, G.Lombard, P.Mollard & D.Mouyon
With the (remote) participations of W.Helou (IO), E.Lerche (ERM), R.Ragona (ERM) and G.Urbanzcyck (ASIPP)

## Slide 2: Where we were at the end of the WEST C4 campaign (1/2)
The WEST ICRH antennas successfully validated
All three antennas operational simultaneously on plasma
  3 MW/few seconds, 5 MW/500ms, and close to 6 MW peak.
Up to 8 MW total RF power (IC + LH) (close to 9 MW peak)
Load resilience confirmed on all antennas
Automatic matching demonstrated
C1 (top)
C2 (bot)

## Slide 3: Where we were at the end of the WEST C4 campaign (2/2)
Work performed during S4 shutdown
1 Voltage probe out of order on Q1  Q1 removed from WEST, cables repaired and hardened  In-vessel fixes for Q4 (not Q2)
Modifications of all vacuum feedthrough (to allow long pulses)
Toroidal phase control with mixed results depending of the antenna  Phase Measurements and Control Loop modified (more in next slides)
Few capacitors couldn’t move due to out of order (obsolete) servopacks  Motors and motorization control fully refurbished
Vacuum feedthrough Internal conductor
Emptying Q4
In-vessel RF cable fix
3 controllers 1 controller
12 new motors
12 new servopacks

## Slide 4
WEST C5 Main Results

## Slide 5: New Toroidal Phase Control (1/2)
Antenna phase measurements and control simplified
  Left side (see from behind the antenna) is the reference
  Right side is frequency-modulated to shift the phase w.r.t. left side
  A FPGA-based PID controls toroidal phase between (top) straps from SL phase request
    Response time to change request is ~50 µs and very robust
Capa 1
Capa 2
Capa 3
Capa 4
Left side HP Amplifier
Right side HP Amplifier
Phase reference
RF source
RF source
Master Oscillator 10MHz reference
Fast optic transmitter
Frequency modulation
V1
V2
V3
V4
V3-V1
PXIe DAQ unit
PID in 3 FPGA Cards
(1/antenna)
Phase measurement
system
Phase request (from Session Leader)
DFCI
Frequency modulation

## Slide 6: New Toroidal Phase Control (2/2)
Very good reliability: +/- 1°
  Phase is slightly disturbed (up to +/- 5°) when multiple antennas are used (crosstalk)
Example on a wriggling plasma
+/- 1cm
+/- 1°
Commissioning, testing
and bewilderment …
LCFS Radal Position
Toroidal Phase
Coupling Resistance
IC Power
1cm

## Slide 7: Differences between magnetic reconstructions persist
ROG Estimation is still different between VACTH (real time) and NICE reconstructions
  Smaller difference in USN vs LSN
  As in C4, coupling is better in USN
   Main explanation for higher coupling resistance observed in USN plasma
   So still some margins to improve coupling
NICE
VACTH

## Slide 8: Operational Difficulties in C5 to Control the Isotopic Ratio (1/3) Evolution during the campaign
Isotopic Ratio went from 35% at the beginning of the C5 campaign to finish at ~5%
H outgassing associated to the new BN tiles installed for C5
Evolution depended of the RF power energy injected and boronization

## Slide 9: Operational Difficulties in C5 to Control the Isotopic Ratio (2/3) IC operation alone
  When >20%, nearly all ICRH power goes into extra radiation.
  When in the “normal” range, radiated fraction 50-60%, similar to LH alone
  Controlled Isotopic ratio challenge in C6
December
January

## Slide 10: Operational Difficulties in C5 to Control the Isotopic Ratio (3/3) LH+IC combined operation
December vs January operation
  Hard to disentangle the effect of the 2nd boronization to the isotopic ratio
  In January, radiating power LH+IC follows same trend than LH or IC alone (50%) (excluding during MHD)
December
January
Comparing to C4, introduction of BN tiles didn’t change the radiated power during RF operation
  No increase of Prad as some could have expected
  Boron limiters can be seriously envisaged
  New antenna limiters are under study (for C7 or C8)

## Slide 11: WEST C5 Statistics – Average Coupled Power C4 vs C5
The maximum coupled power achieved in C5 was not higher than in Q4
But somewhat a faster ramp-up
Highest power achieved at lower Ip than in C4
  Despite coupling generally most difficult at such Ip
  for PIC ~ PLH ~3 MW both
C5 RF Commissioning
C4
C5
nl~5.3
ROG 2cm vs 4cm
No LH vs ~same LH
(average on pulse)

## Slide 12: …C5 Campaign was marked by a higher Copper impurity level
Despite similar range of RF Power, higher Cu level
Directly affects operational limits (interlocks for LH Power)
Origin is still unknown
C4
C5

## Slide 13: The Control Room Question #1: Does ICRH trigger more Cu impurity than LH?
when RF systems operated independently, Copper impurity level is mainly driven by total power
  No specific effect of ICRH in the release of Cu impurity
Much higher values during LH+IC (except after boronization)
  Cu impurity increases dramatically due to some interaction btw LH & IC (independently of the order LH/IC)
Physical mechanisms unclear yet, to be investigated in C6
Lower points: Just After boro

## Slide 14: The Control Room Question #2: Does Q4 generates more impurities than other antennas?
Rather unclear (to me) if intrinsic to Q4 or ext. consequence
  Egg or chicken problem
In this example #56895 (Q1+Q2) vs #56894 (Q1+Q2+Q4)
  180° Phasing OK, Voltage Magnitudes & Balancing OK
  ne rises faster on 56895 (Outgassing of what?) -> Te drops faster,
  MHD is triggered (->Rext oscillates) and silver impurity levels rise
  Note that frad is similar (~60%) before and during IC
  Transport effect or additional sources effect?
  Cu Impurity level similar before MHD (Ag slightly higher due to +0.5MW
Remarks
  Limited time allowed for power ramp-up on Q4 vs Q1 & Q2…
  Outgassing due conditioning effect?
  Proper dedicated time required to ramp-up antennas for a given scenario…
  Real-Time Silver Impurity Signal can be used as an IC power interlock. To be tested in C6.
MHD
frad
nl
Te
Cu19
Ag19
PIC
MHD

## Slide 15: RF Modelling: Towards a Digital Twin Representation of the Antennas
Goal: Help IC Operators in Control Room
  Future work: post pulse measurement interpretations & next pulse predictions
Antenna Model + Jupyter Notebook + Voilà  GUI for IC Operator
WEST ICRH Antenna Model
Validated against antenna measurements
Opens-source, used by collaborators (PPPL) for coupling modelling (Petra-M)
  First results show good relative results between experiments & modelling
  Work on-going to match experimental values from plasma profiles & equilibrium

## Slide 16: Work performed under the hood
Several hardware problems have been fixed during the campaign
Often not visible, despite being critical, here is a non-exhaustive list:
  Unbalanced power between left and right side of Q1:
    Defect in one of the RF oscillator. To be replaced for C6.
  Up to 9mm Radial Misalignment between left and right sides of Q2
    Due to an incorrect setup of the pressure between hydraulic cylinder. Fixed 18/01.
  Various repairs at plant:
    Anode Current Sensor Voltage Power Supply Repaired
    Leaking Pressurized Air Network Refurbished
    Low Power Stage Anode Capacitor replaced (no more spare part)
    …

## Slide 17
Post C5 Visual Inspections

## Slide 18: ICRH Antennas after C5
Antennas Faraday Screen “copperized”
  Silver coated now looks more orange than white.
  Does IC power remobilize copper dusts and non-adherent coatings?

## Slide 19: Hot Spot on Q2 due to a local change in the Q2 strap
Hot spot appear on Q2 antenna during C5 campaign RF restart
Inspection reveal real surface feature
  FS bars clean
  Investigations on-going…
Before C5
After C5

## Slide 20: Q4
Right side of the Q4 overheated during C5
  But no new damage on right lateral limiter (tbc)
  Due to plasma start-up at the beginning of C5? Not inspected with AIA during C5, no clue…
  Explanation for the silver production associated with Q4?
Q4 removed from the machine during S5
  Planned before & required to change divertor elements
  Investigations on-going…
Before C5
After C5

## Slide 21
Perspectives for S5 shutdown and C6

## Slide 22: Remaining Work
Work during S5 shutdown
Validate inner conductors water cooling setup (allows >30s)
  Setup compatibility with WEST baking mode
Change voltage probe cables of Q4 antenna + change RF cables to CODAC
Repair Q2 strap? Clean Q4 Faraday Screen?
…
Planned work for C6
Implement VUV Silver signals as security (like copper for LH)
Validate the automatic matching with the new capacitor motorization system (not enough time in C5)
Develop local gas puffing scenarios with the full pumping capability
Plasma start-up assisted with ICRH (WP-TE experiment)
Relative Antenna Phasing Experiment (WP-TE experiment)

## Slide 23: Preliminary Conclusions for C5 Campaign
PRELIMINARY
Antennas Phase Control Validated
  Good Reliability of +/- 1°
  Some work remain for automatic matching with the new capacitor motorization system
Operational Difficulties in C5 to Control the Isotopic Ratio
  Real issue: varied from 40% to 0%...
  Lead to extra radiated power and probably other problems -> to be avoided
Issues with copper?
  Plasma facing components, especially antennas, copper coated
Separated IC or LH operation is OK, but combined operation leads to additional difficulties
  Work is on going to understand how to improve the situation

## Slide 24: Thank you for your attention

## Slide 25
Spare slides
Pas directement lié au sujet

## Slide 26: New Capacitor Motorization System
3 controllers 1 single controller
12 new motors
12 new servopacks
Motor coders
Motor command
RS232
STOR / ETOR
RF presence (True/False)
Capacitor coders
API
CODAC
Controller
Velocity requests (+/- 10v)
servopacks

## Slide 27: Inside Antenna Boxes
Much more copper (?) deposition inside Q1 and Q4 than Q2
  Hypothesis: Q2 is less connected to LH launchers than Q1 and Q4?
Q2
Q1
Q4

## Slide 28: Evolution of Copper, Iron and Silver Impurity
Averaged during RF operations
  Vertical lines: Pulse with ICRH power

## Slide 29: Radiated Power
Between 40 to 60%
  But
56626
56651
56601
56625

## Slide 30: Despite similar range of RF power…
C4
C5

## Slide 31: 56984
Despite similar voltages, Q4 antenna generated more impurity that Q1 and Q2

## Slide 32: The Control Room Dilemma: How to combine IC & LH properly?
Examples with the last high confinement session (nl~4)
56899: LH 1st, then IC
56896: IC 1st, then LH
150/4MW=
100/2MW=